## Slide 1: Image Fusion of satellite images
Jasmine Puente
Brenda Gonzalez
Faculty Advisor : Dr. Helmut Knaust

## Slide 2: What is Image Fusion and why is it important?
Process of combining information from two or more images to form a final fused image
We will be using a low resolution multispectral satellite image and a high resolution panchromatic satellite image.
It is more cost efficient
The resulting Multispectral satellite images are used to
  gather agriculture and resource data
  gather information for urban and land development

## Slide 3
Berlin Satellite Images
256 x 128
1024 x 512

## Slide 4: Manipulating Matrices
Images are stored into the computer as large matrices
Each entry corresponding from 0 (black) to 255 (white)
For color images, each entry has a vector containing three entries
We can manipulate the image by manipulating the matrix

## Slide 5: Color Transfer Method
Y-Cb-Cr
It is a color space
It is used to encode color images based on human perception

## Slide 6
Enlarged the color satellite image and separated it into its luminance and chrominance channels

## Slide 7: Discrete Wavelet Transform Method
We used the Haar wavelet.
Applied the Haar wavelet transform to each channel and the grey scale image
Applied multiple iterations to the blur

## Slide 8
Due to the blur being downsized, we were limited on the amount of iterations we could compute.
2 iterations

## Slide 9
4th Haar Iteration
6th Haar Iteration
5th Haar Iteration
7th Haar Iteration

## Slide 10: Discrete Wavelet Frame Transform Method
Applying these filters to the image would not downsize the blur
Blur : applied the low pass filter to the rows and columns
Vertical edges : applied the low pass filter to the rows and the high pass filter to the columns
Horizontal edges : applied the high pass filter to the rows and the low pass filter to the columns
Diagonal edges : applied the high pass filter to the rows and columns

## Slide 11: Improvement of spatial characteristics
Peak Signal to Noise Ratio (PSNR)
Measures how similar two images are by comparing each entry
Chart: 
| EMSI | 1 Haar | 2 Haar | 3 Haar | 4 Haar | 5 Haar | 6 Haar | 7 Haar | 8 Haar
image w/ori | 19.285 | 20.6524 | 25.2214 | 29.0078 | 30.8167 | 30.584 | 29.9371 | 29.4328 | 28.9051
Y of image with GS | 19.4094 | 19.7902 | 19.6536 | 19.8839 | 20.2101 | 20.5058 | 20.7833 | 21.0135 | 21.3176
image with EMSI | 24.9657 | 20.5615 | 19.648 | 19.3133 | 19.1844 | 19.1023 | 19.0538 | 18.9957
Chart: 
| EMSI | 1 DWFT | 2 DWFT | 3 DWFT | 4 DWFT | 5 DWFT | 6 DWFT | 7 DWFT | 8 DWFT | 9 DWFT | 10 DWFT | 11 DWFT | 12 DWFT | 13 DWFT | 14 DWFT | 15 DWFT
image w/ori | 19.285 | 22.4274 | 24.1716 | 25.4224 | 26.3777 | 27.1339 | 27.7487 | 28.2593 | 28.6909 | 29.0554 | 29.3762 | 29.6569 | 29.9046 | 30.1243 | 30.3203 | 30.4959
Y of image with GS | 19.4094 | 21.9449 | 23.3083 | 24.2657 | 24.9909 | 25.5646 | 26.0329 | 26.4254 | 26.76 | 27.0494 | 27.3043 | 27.5306 | 27.7329 | 27.9147 | 28.0802 | 28.23
image with EMSI | 26.2658 | 23.7834 | 22.6065 | 21.9044 | 21.4378 | 21.11 | 20.8614 | 20.6729 | 20.5248 | 20.4048 | 20.3061 | 20.2236 | 20.1535 | 20.0933 | 20.041
YCbCr PSNR
28.8008 img w/ori

## Slide 12
Entropy
Measures length of shortest representation to encode the information
Chart: 
| EMSI | 1 Haar | 2 Haar | 3 Haar | 4 Haar | 5 Haar | 6 Haar | 7 Haar | 8 Haar
fused image | 7.597 | 7.6964 | 7.7857 | 7.7559 | 7.7343 | 7.7241 | 7.7176 | 7.7122 | 7.7025
Fused R | 7.5534 | 7.6731 | 7.7681 | 7.7329 | 7.6983 | 7.6831 | 7.6729 | 7.6699 | 7.6619
Fused G | 7.5314 | 7.6234 | 7.723 | 7.6958 | 7.6711 | 7.6622 | 7.656 | 7.6566 | 7.6574
Fused B | 7.5861 | 7.6961 | 7.781 | 7.7503 | 7.7347 | 7.7249 | 7.714 | 7.6972 | 7.7025
Chart: 
| EMSI | 1 DWFT | 2 DWFT | 3 DWFT | 4 DWFT | 5 DWFT | 6 DWFT | 7 DWFT | 8 DWFT | 9 DWFT | 10 DWFT | 11 DWFT | 12 DWFT | 13 DWFT | 14 DWFT | 15 DWFT
fused image | 7.597 | 7.6134 | 7.6268 | 7.6362 | 7.6446 | 7.6521 | 7.6585 | 7.6643 | 7.6692 | 7.6735 | 7.6773 | 7.6806 | 7.6835 | 7.6861 | 7.6884 | 7.6906
fused R | 7.5534 | 7.5873 | 7.603 | 7.6132 | 7.6188 | 7.6291 | 7.6353 | 7.6405 | 7.645 | 7.6488 | 7.652 | 7.6549 | 7.6573 | 7.6595 | 7.6613 | 7.663
fused G | 7.5314 | 7.534 | 7.5527 | 7.5662 | 7.5769 | 7.5858 | 7.5932 | 7.5995 | 7.6049 | 7.6094 | 7.6134 | 7.6169 | 7.6199 | 7.6225 | 7.6251 | 7.6272
fused B | 7.5861 | 7.6101 | 7.6197 | 7.6262 | 7.6331 | 7.6396 | 7.6456 | 7.6513 | 7.6564 | 7.6607 | 7.6648 | 7.6684 | 7.6716 | 7.6745 | 7.6772 | 7.6796
YCbCr Entropy
7.92296 fused image

## Slide 13: Preservation of spectral characteristics
Correlation Coefficient
Determines the degree to which two variables are associated
Chart: 
| EMSI | 1 Haar | 2 Haar | 3 Haar | 4 Haar | 5 Haar | 6 Haar | 7 Haar | 8 Haar
image w. ori | 0.85856 | 0.89971 | 0.9679 | 0.9872 | 0.99181 | 0.99125 | 0.98963 | 0.9882 | 0.98655
image w/ EMSI | 1 | 0.95948 | 0.89884 | 0.87205 | 0.85834 | 0.85196 | 0.84776 | 0.84519 | 0.84133
fused R and Ori R | 0.85238 | 0.89528 | 0.9664 | 0.98682 | 0.99218 | 0.99215 | 0.9914 | 0.99043 | 0.98982
fused G and Ori G | 0.84695 | 0.89275 | 0.96796 | 0.99011 | 0.99729 | 0.99881 | 0.99917 | 0.9992 | 0.99918
fused B and Ori B | 0.80029 | 0.9021 | 0.96698 | 0.98412 | 0.98613 | 0.9832 | 0.97891 | 0.97567 | 0.97158
Chart: 
| EMSI | 1 DWFT | 2 DWFT | 3 DWFT | 4 DWFT | 5 DWFT | 6 DWFT | 7 DWFT | 8 DWFT | 9 DWFT | 10 DWFT | 11 DWFT | 12 DWFT | 13 DWFT | 14 DWFT | 15 DWFT
image w. ori | 0.85856 | 0.93424 | 0.9575 | 0.9689 | 0.97546 | 0.97964 | 0.98148 | 0.98458 | 0.98613 | 0.98733 | 0.9883 | 0.98909 | 0.98975 | 0.9903 | 0.99077 | 0.99118
Y of fused with GS | 0.84803 | 0.92976 | 0.95501 | 0.96742 | 0.97461 | 0.97922 | 0.98143 | 0.98472 | 0.98649 | 0.98788 | 0.98901 | 0.98994 | 0.99073 | 0.9914 | 0.99198 | 0.99248
image w/ EMSI | 1 | 0.96772 | 0.94334 | 0.92657 | 0.9146 | 0.90577 | 0.8985 | 0.89393 | 0.88985 | 0.88657 | 0.88387 | 0.88163 | 0.87943 | 0.87813 | 0.87673 | 0.87551
fused R and Ori R | 0.85238 | 0.93118 | 0.9554 | 0.96726 | 0.97409 | 0.97845 | 0.97993 | 0.9836 | 0.98524 | 0.98625 | 0.98755 | 0.98839 | 0.98909 | 0.98968 | 0.99019 | 0.99063
fused G and Ori G | 0.84695 | 0.93008 | 0.95617 | 0.9681 | 0.9753 | 0.97989 | 0.98372 | 0.98534 | 0.98708 | 0.98845 | 0.98955 | 0.99046 | 0.99123 | 0.99188 | 0.99244 | 0.99292
fused B and Ori B | 0.80029 | 0.93556 | 0.95786 | 0.96878 | 0.97505 | 0.97903 | 0.98042 | 0.98366 | 0.98511 | 0.98616 | 0.98704 | 0.98774 | 0.98832 | 0.98879 | 0.98918 | 0.98951
YCbCr correlation coefficient
0.99695 img w/ori

## Slide 14
Spectral Discrepancy
Measures the difference in the intensities of the corresponding spectral bands
Chart: 
| EMSI | 1 Haar | 2 Haar | 3 Haar | 4 Haar | 5 Haar | 6 Haar | 7 Haar | 8 Haar
Fused R w/ Ori R | 19.4245 | 16.4669 | 9.5053 | 6.4955 | 5.2359 | 5.3097 | 5.5317 | 5.8119 | 5.9948
Fused G w/ Ori G | 18.9899 | 15.9896 | 8.8062 | 5.3841 | 3.4376 | 2.8307 | 2.3766 | 2.6618 | 2.3829
Fused B w/ Ori B | 19.316 | 16.4436 | 9.8171 | 7.4065 | 7.0641 | 7.7741 | 8.6884 | 9.3515 | 10.2742
Chart: 
| EMSI | 1 DWFT | 2 DWFT | 3 DWFT | 4 DWFT | 5 DWFT | 6 DWFT | 7 DWFT | 8 DWFT | 9 DWFT | 10 DWFT | 11 DWFT | 12 DWFT | 13 DWFT | 14 DWFT | 15 DWFT
Fused R w/ Ori R | 19.4245 | 13.6349 | 11.1563 | 9.6546 | 8.6532 | 7.9426 | 7.5923 | 7.0115 | 6.6927 | 6.4354 | 6.2239 | 6.0472 | 5.8979 | 5.7698 | 5.6589 | 5.562
Fused G w/ Ori G | 18.9899 | 13.2167 | 10.697 | 9.1458 | 8.0923 | 7.332 | 6.9734 | 6.3081 | 5.9465 | 5.649 | 5.3997 | 5.1878 | 5.0054 | 4.8466 | 4.7069 | 4.5829
Fused B w/ Ori B | 19.316 | 13.6062 | 11.1835 | 9.7377 | 8.7894 | 8.1297 | 7.7382 | 7.2912 | 7.0144 | 6.807 | 6.6325 | 6.4906 | 6.3737 | 6.2766 | 6.1953 | 6.127
YCbCr Spectral Discrepancy
7.2278 red channels
6.83007 green channels
7.93516 blue channels

## Slide 15: Close-up
Original
Y-Cb-Cr
DWFT (15th iteration)
4th Haar Iteration

## Slide 16: Conclusion and Future Research
The DWFT seems to provide the best quality of the fused image
Due to the amount of computations needed to compute the DWFT, it is not as practical as the others.
Further research could include
  Computing more iterations using the DWFT method
  Manipulating the color transfer method by applying discrete wavelet transform methods along with the color transfer methods

## Slide 17: Acknowledgments
The National Security Agency (H98230-13-1-0270)
The National Science Foundation(DMS-1156582)
Dr. Helmut Knaust
All of you

## Slide 18: Literature Cited
Han, S.S., Li, H.T., Gu, H.Y., 2008. The study on image fusion for high spatial resolution remote
sensing images. The International Archives of the Photogrammetry, Remote Sensing and
Spatial Information Sciences. Vol. XXXVII. Part B7.
(2) Li S. and Kwok J.T. and Wang Y. (2002) Using the discrete wavelet frame transform to merge
Landsat TM and SPOT panchromatic images. Information Fusion 3: 17-23.
(3) W.J. Carper, T.W. Lilesand, R.W. Kieffer. The use of Intensity-Hue-Saturation transformation for
merging SPOT panchromatic and multispectral image data, Photogrammetric Engineering
and Remote Sensing 56 (4) (1990) 459-467.
(4) Yakhdani M.Fallah and Azizi A. (2010) Quality Assessment of Image Fusion Techniques for
Multisensor High Resolution Satellite Images (Case Study: IRS-P5 and IRS-P6 Satellite Images).
In. Wagner W., Szekely, B. (eds.): ISPRS TC VII Symposium – 100 years ISPRS, Vienna, Austria,
July 5-7, 2010, IAPRS, Vol. XXXVIII, Part 7B: 205-208.
(5) Zhenhua Li, Zhongliang Jing, Xuhong Yang, Shaoyuan Sun. Color transfer based remote sensing
image fusion using non-separable wavelet frame transform. Pattern Recognition Letters 26
(2005): pp. 2006-14.